Color IR Camera with 24 Infra-Red LEDs 1/3” Sony Super HAD CCD 420 TV lines 0.1 Lux (CDS Sensor on 0.00 Lux) 12V DC Weather-proof Sunshield & mounting bracket included

Model No. NVC-IR024 Image Pick-up device 1/3” Color SONY Super-HAD CCD Effective Pixels 510(H) x 492(V) Resolution 420 TV lines Sync. System Internal Scanning System 525 lines, 2:1 interlace Scanning Frequency H:15.734KHz, V:59.94Hz S/N Ratio More than 45dB Video Output VBS Composite Video(1.0Vp-p, 75ohm) Gamma Correction γ = 0.45 Electronic Shutter Auto 1/60 ~ 1/100,000 sec. Lens 3.6mm Minimum Illumination 0.1 lux (with CDS sensor on 0.00 lux) Number of Infra-red LED 24 IR LEDs Power Supply DC 12V Dimensions (inch.) 2.2”(W) x 2.4”(H) ( 3.8”(L) Weight 1.4 lbs